## Slide 1: Component based software development & software middleware
Lorenzo Natale
iCub Facility
Istituto Italiano di Tecnologia, Genova, Italy
Winter School on Humanoid Robot Programming
Santa Margherita Ligure, 30 Jan- 8 feb 2017

## Slide 3
Due to a human programming error, the robot fell when transitioning from the driving task to the egress task (the foot throttle controller wasn’t turned off). This caused the robot to the fall and faceplant out of the car onto the asphalt (source: http://drc.mit.edu/)

## Slide 4: System Integration

## Slide 5: Key issues
  Complexity: distributed processing, heterogeneous systems, noise, real-time
  Asynchronous development
  Variability: various scenarios and platforms
  Fast prototyping
  Lack of standards
  Fluctuation in hardware and algorithms, lots of open questions

## Slide 6: Approach
Major cost in software development is debugging, recycling code is key
Component driven software development
Middleware: factor out platform specificities
  Hardware (robot abstraction layer)
  Communication
  Operating system
  Parameters
  Computing infrastructure
Recently: test driven development

## Slide 7: Component driven software development
Computation
Communication
Configuration
Coordination
Composition
What we are interested in
Dependent on the hardware, network topology
Application dependent
BRICS Component Model, 2013

## Slide 8
output myAlgorithm(input)
{
...
data=readSensor() //call device driver
out = call alg1(data)
…
out = call alg2(data)
controlMotors(out) //call device driver
…
}
output alg1(input)
{code}
output alg2(input)
{code}

## Slide 9
output myAlgorithm(input)
{
data=readSensor() //call device driver
out = query(alg1, data)
…
out = query(alg2, data)
controlMotors(out) //call device driver
…
}
output alg1(input)
{code}
output alg2(input)
{code}
Program2
alg2()
middleware
Program2
alg1()
middleware
myAlgorithm()
Program1
middleware
Operating System facilities: Network or shared memory
drivers
Robot
middleware
hardware

## Slide 10: Component driven development
Modular software: simple structure, data encapsulation, interface
Reconfigurable components
Reduced coupling: interaction between components happens through pre-defined standards (no direct inclusion of header files)
Language independent

## Slide 11: Middleware: general concepts
Information sharing model
Serialization, Interface Definition Language
Communication model, timing
Data persistency
Hardware abstraction layer

## Slide 12: Information sharing model
Data ports
Services
Data centric (blackboard)
Blackboard
Component
Component
Component
Client
Server
Client
Component
Component

## Slide 13: Serialization
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
…
Point3D
Class Point3D
{
int x;
int y;
int z;
}
Network
300
200
100
…
…
300
Computer 1
Computer 2

## Slide 14: Serialization
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
More: 0x200
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
More:0x300
Point3D
Class Point3D
{
int x;
int y;
int z;
char *more;
}
Network
300
200
100
…
…
300
Computer 1
Computer 2
999
???
999

## Slide 15: Interface Definition Language
Allows describing types
A compiler generate required code to define the type, including serialization functions
Language independent, if the middleware is cross-language
point3d.thirft
struct Point3D {
1: i32 x;
2: i32 y;
3: i32 z;
}
Point3D.h/Point3D.cpp
class Point3D
{
int x;
int y;
int z;
serialize();
deserialize();
}
IDL compile

## Slide 16: Communication model
Remote Procedure Calls (RPC)
  Remote invocation of an object
  Synchronous nature (although variant exists)
Publish/Subscribe
  Space, time, synchronization decoupling

## Slide 17: Timing in RPC

## Slide 18: Decoupling in publish-subscribe
Space decoupling: the interaction parties do not need to know each other; publisher publish events through an event service and the subscribers get these events indirectly through the event service
Time decoupling: interaction parties do not need to be actively participating in the interaction at the same time, publisher might publish events while subscribers is disconnected and subscribers might get notified of an event while the original publisher is disconnected
Synchronization decoupling: publishers are not blocked while producing events and subscribers can get asynchronously notified (through callback) of the occurrence of the event while performing concurrent activity
Eugster, et al., The Many Faces of Publish/Subscribe, 2003.

## Slide 19
Eugster, et al., The Many Faces of Publish/Subscribe, 2003.

## Slide 20: Data storage (persistency)
What happens when the sender is faster than the receiver?
Buffering:
  First In First Out (messages are queued, at the cost of latency)
  Oldest Packet Drop: minimize latency, drop messages if required

## Slide 21: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
0x204
0x208
0x20C
0x210
Z:???
…
Network
300
200
100
…
…
300
Computer 1
Computer 2
Component1

## Slide 22: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
0x204
0x208
0x20C
0x210
Z:???
…
Network
300
200
100
…
…
300
Computer 1
Computer 2
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
…
Component1
Component2

## Slide 23: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
0x204
0x208
0x20C
0x210
Z:???
…
Network
300
200
100
…
…
300
Computer 1
Computer 2
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
…
Point3D::deserialize()
Component1
Component2

## Slide 24: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
Point3D::serialize()
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
0x204
0x208
0x20C
0x210
Z:???
…
Network
300
200
100
…
…
300
Computer 1
Computer 2
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
…
Not necessary copies! (overhead, especially for large data like images)
Point3D::deserialize()
Component1
Component2

## Slide 25: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
…
200
100
…
…
Point3D::deserialize()
…
X:???
Y:???
0x204
0x208
0x20C
0x210
Z:???
…
Network
…
…
300
Computer 1
Computer 2
…
X:???
Y:???
4 bytes
0x204
0x208
0x20C
0x210
Z:???
…
Not necessary copies! (overhead, especially for large data like images)
Zero-copy
Point3D::deserialize()
Component1
Component2

## Slide 26: Reducing latency/memory copies
X:100
Y:200
Z:300
4 bytes
0x100
0x104
0x108
0x10C
…
…
Point3D
…
200
100
…
…
…
X:???
Y:???
Z:???
…
Network
Computer 1
Computer 2
Not necessary copies! (overhead, especially for large data like images)
Zero-copy
Copy-once
Component1 private memory
Component2 private memory
Component1
Component2
Shared memory

## Slide 27: Which Middleware
Robot Operating System (ROS)
YARP
OROCOS
SmartSoft
CORBA
ICE
OMG DDS
Many others: OpenRDK, Mira…

## Slide 28: ICE/CORBA/COM-DCOM
Remote object invocation
An object-oriented specification language
Synchronous/asynchronous
May have deployment tool, versioning etc..

## Slide 30: OROCOS: Open Robot Control Software
Kinematics and Dynamics Library and Bayesian Filtering Library
Real-Time Toolkit: it provides the infrastructure and the functionalities to build real-time robotics applications in C++
OROCOS Component Library: ready to use components
Coordination
Communication
Configuration

## Slide 32: Component lifecycle

## Slide 33: Model Driven Software Engineering
Models can make a particular system or phenomenon easier to understand, quantify, visualize simulate, or predict
Models are used in many fields of engineering, either graphical (architecture) or textual (equations of physics)
They are created using modeling languages (Domain specific languages, or DSLs)
Software engineering can greatly benefit from the use of models because software and models have the same nature, and it is easy to automate the process of software generation and analysis
Example: SmartSoft MDE toolchain
From: D. Brugali, Model-Driven Software Engineering in Robotics, IEEE Robotics and automation magazine, Sept. 2015

## Slide 34
<<component>>: elemental components
<<subsystem>>: composite components
Each component is characterized by a set of ports, interaction point with other components
Provide and requested interfaces
Connectors: Caller/Provider, Publisher/Subscriber

## Slide 35
From an architectural model it is possible to generate platform specific code templates (that implement the specified architecture and include calls to the target framework, i.e. the middleware)
Code templates is complemented with code provided by the developer (specific robot functionalities) to produce executable code
Challenges: hardware requirements, real-time constraints, embedded and distributed systems, many application scenarios, dynamic interaction with the environment
DSL for robotics should include: timing constraints, communication infrastructure, allocation of threads and processes to difference processors

## Slide 36: YARP/ROS
Components are executables which communicate through well-defined named objects called Ports (YARP), Topics (ROS)
A central server (yarpserver/roscore) keeps tracks of names and allows Ports/Topics to be reachable
Communication is peer-to-peer between Ports/Topics

## Slide 37: YARP approach
Simplified form of publish-subscribe
  Observer patter: subscribers register their interest directly with publishers, which mange subscriptions and sends events
Communication is asynchronous or synchronous
Space decoupling
Connections are dynamic
Remote procedure calls for server-client type of communication
See also:
YARP: Yet Another Robot Platform, G. Metta, P. Fitzpatrick, L. Natale, 2006
Design of Dynamically Reconfigurable Real-time Software Using Port-Based Objects, Stewart et al., 1997

## Slide 38
yarpserver
Register /camera, 192.168.1.4:10001
Register /cmd, 192.168.1.4:10002
Query /camera …
Query /cmd …
/camera
/cmd
connect /camera /source2 mcast
/source2
Register /source, 192.168.1.3:10001
Register /pos, 192.168.1.3:10002
Query /camera …
Query /cmd …
/source
/pos
udp/tcp
udp
mcast
connect /pos /cmd
connect /camera /source
Process 1
Process 2
Process 3

## Slide 39: YARP/ROS comparison
YARP
Run-time reconfiguration of connections
Pluggable protocols and devices
Multicast for efficient one-to-many communication
Multi-platform
QoS, channel prioritization
LGPL/GPL
Smaller community
No packet management
ROS compatible protocol
ROS
Strongly typed
Rich set of libraries and tools
Eco-system, very active community
Packet management
BSD license
Ubuntu based
Restricted set of protocols
All connections from a topic use the same protocol

## Slide 40: Data Distribution Service
Omg standard (int. consortium of many companies, proposers of various standards, e.g. UML, CORBA,
Data (as opposed to message) centric
Share data even between time-decoupled publishers and consumers
Interest-based filter on content, age and/or lifecycle
DDS dynamically discovers publishers and subscribers (no central server naming server), determines data they share and Quality of Service (QoS)
  For example, if a subscriber requires an update every 10ms and its matched publisher does not deliver, the system declares an error, enabling remedial action
  QoS: urgency, importance, reliability, persistence, and liveliness
It is built on two standards: real-time wire protocol (RTPS) and C++ API
Several implementations exists: proprietary as well as open source (opensplice, opendds, RTI connext)
ROS 2.0 is going to be based on DDS

## Slide 41: Robot Abstraction Layer
…
…
read encoders
read IMU
read FT
…
get image
...
set position
Loops on board
Robot Interface
Robot

## Slide 42: Robot Abstraction Layer
…
…
read encoders
read IMU
read FT
…
get image
...
set position
.
External loops
Robot Interface
…
…
read encoders
read IMU
read FT
…
get image
...
set position
Loops on board
Network
Network Stub
Network Stub
Robot Interface
Robot

## Slide 44: Similar approachers
ROS Control
H-ROS

## Slide 45: Why Channel Prioritization (QoS)
HOST1
Robot

## Slide 46
HOST1
Robot
switch
20% load

## Slide 47: Channel prioritization
HOST1
Robot
switch
HOST2
Determinism is affected by:
Thead scheduling (CPU usage)
Packet conflicts (network usage)
Bottlenecks

## Slide 48
Approach: improve determinism by increasing thread priorities and reducing network bottlenecks using QoS
> prop sched policy 1 priority 30
> prop set qos priority HIGH
Paikan et al., A Best-Effort Approach for Run-Time Channel Prioritization in Real-Time Robotic Application IROS 2015

## Slide 49
HOST1
Robot
switch
20%/70% load
With priority (20%)
Standard YARP (20%)
With priority (70%)
Standard YARP (70%)

## Slide 50: An application

## Slide 51: References
Ali Paikan, Silvio Traversaro, Francesco Nori and Lorenzo Natale, "A Generic Testing Framework for Test Driven Development of Robotic Systems", In Lecture Notes in Computer Science (MESAS15), Springer, pp. , 2015
Paikan, A., Domenichelli, D., and Natale, L., Communication channel prioritization in a publish-subscribe architecture, in Proc. Software Engineering and Architectures for Realtime Interactive Systems Workshop, Arles, France, 2015.
Paikan, A., Tikhanoff, V., Metta, G., and Natale, L., Enhancing software module reusability using port plug-ins: an experiment with the iCub robot, in Proc. IEEE/RSJ International Conference on Intelligent Robots and Systems, Chicago, Illinois, 2014.
Fitzpatrick, P., Ceseracciu, E., Domenichelli, D., Paikan, A., Metta, G., and Natale, L., A middle way for robotics middleware, Journal of Software Engineering for Robotics, vol. 5, no. 2, pp. 42-49, 2014.
Paikan, A., Fitzpatrick, P., Metta, G., and Natale, L., Data Flow Port's Monitoring and Arbitration, Journal of Software Engineering for Robotics, vol. 5, no. 1, pp. 80-88, 2014
Metta, G., Fitzpatrick, P., Natale, L., YARP: Yet Another Robot Platform, International Journal of Advanced Robotics Systems, special issue on Software Development and Integration in Robotics, Volume 3, Issue 1, pp. 43-48, March 2006
Patrick Th. Eugster, Pascal A. Felber, Rachid Guerraoui, and Anne-Marie Kermarrec. 2003. The many faces of publish/subscribe. ACM Comput. Surv. 35, 2 (June 2003), 114-131.
David, B. Stewart, Richard, A. Volpe, Pradeep, K. Khosla, Design of Dynamically Reconfigurable Real-Time Software Using Port-Based Objects, IEEE Trans. On Software Engineering, 23(12), 1997
Dušan Bálek, František Plášil, Software Connectors and Their Role in Component Deployment, New Developments in Distributed Applications and Interoperable Systems, 70, 2002, pp. 69-84.
Farhad Arbab: Reo: a channel-based coordination model for component composition. Mathematical Structures in Computer Science 14(3):329--366, 2004.
D. Brugali, Model-Driven Software Engineering in Robotics, IEEE Robotics and automation magazine, Sept. 2015

## Slide 52
Questions?

## Slide 53: Threads and scheduling, quick overview
Issues:
Scheduling and interrupt latency
Certain operations may be blocking i.e. not preemptable (usually system calls)
System calls: file management, process management, I/O, memory requests, communication (shared memory), error handling

## Slide 54: Interfaces
Robot abstraction layer: interfaces to motors and sensors minimize the impact of changes in the hardware
Custom interfaces and data types (Thrift IDL)
point3d.thirft
struct Point3D {
1: i32 x;
2: i32 y;
3: i32 z;
}
adder.thirft
service Adder {
/** … */
i32 get_answer();
/** … */
bool set_answer(1:i32 val)
/** … */
i32 add (1:i32 x);
}

## Slide 55: Carrier plugins
YARP Camera /camera
YARP
yarp connect /camera /receiver
receiver
YARP
yarp connect /65.52.88.202:5159 /receiver mjpeg
MJPG camera
http://65.52.88.202:5159
receiver
YARP
Camera.msg
yarp connect /image@/camera /receiver
ROS Camera
Node: /camera
Topic: /image
receiver

## Slide 56: More on YARP-ROS (1)
YARP protocols for rostcp and xmlrpc
Compatibility with roscore
YARP can interpret ROS messages, statically or dynamically
Extended YARP’s API (nodes, publishers, subscribers)
yarpidl_rosmsg
Pose.msg
Twist.msg
Pose.h
Twist.h
#include "Pose.h"
#include "Twist.h"
/* create ROS Node /controller */
yarp::os::Node node("/controller");
/* create a subsriber for Pose.msg */
yarp::os::Subscriber<Pose> pose;
/* subscribe to /turtle1/pose */
pose.topic("/turtle1/pose");
/* create a publisher for Twist.msg */
yarp::os::Publisher<Twist> cmd;
/* publish to /turtle1/cmd_vel */
cmd.topic("/turtle1/cmd_vel");
/* read a new value from the topic */
pose.read(p);
/* publish the command */
cmd.write(t);

## Slide 57
yarpidl_rosmsg –name /typ@yarpidl
C:\yarp read /turtle1/pose@/reader
yarp: Receiving input from /turtlesim to
/turtle1/pose-@/reader
5.544445 5.544445 0.0 0.0 0.0
5.544445 5.544445 0.0 0.0 0.0
...
[type] BEGIN turtlesim/Pose
[type] float32 x
[type] float32 y
[type] float32 theta
[type] float32 linear_velocity
[type] float32 angular_velocity
[type] END turtlesim/Pose
turtlesim/Pose?
ROS types
$ rosrun turtlesim turtlesim_node
[ INFO] [1444722896.501281004]: Starting turtlesim with node name /turtlesim
turtlesim/Pose
[Data]
YARP machine
ROS machine
ROS+YARP machine

## Slide 58
Whole-Body Modules
RobotInterface
Locomotion
Module
Manipulation
Modules
Perception
Pilot
Interface
Footstep &
Trajectory Planners
Coman
Walkman

## Slide 59
ROS gmapping, RVIZ, Gazebo

## Slide 60: Port monitor
Paikan, A. et al, Data Flow Port's Monitoring and Arbitration, JOSER 2014

## Slide 61
Paikan, A. et al, Data Flow Port's Monitoring and Arbitration, JOSER 2014
if (C1.certainty > 0.9)
accept(C1)
else
accept(C2)
arbitration
coordination
if (check(C1)
dispatch(event)
filtering
C1=filter(C1)
logging
dispatch(C1)
monitoring delays, QoS
If (C1)
T1=getTime()

## Slide 62: Why Channel Prioritization (QoS)
HOST1
Robot

## Slide 63
HOST1
Robot
switch
20% load

## Slide 64: Channel prioritization
HOST1
Robot
switch
HOST2
Determinism is affected by:
Thead scheduling (CPU usage)
Packet conflicts (network usage)
Bottlenecks

## Slide 65
Approach: improve determinism by increasing thread priorities and reducing network bottlenecks using QoS
> prop sched policy 1 priority 30
> prop set qos priority HIGH
Paikan et al., A Best-Effort Approach for Run-Time Channel Prioritization in Real-Time Robotic Application IROS 2015

## Slide 66
HOST1
Robot
switch
20%/70% load
With priority (20%)
Standard YARP (20%)
With priority (70%)
Standard YARP (70%)

## Slide 67
HOST1
Robot
switch
HOST2
20%/70% load

## Slide 68: Comparison with DDS

## Slide 69: Comparison with DDS

## Slide 70: An application

## Slide 71: Acknowledgements
Ali Paikan (YARP, port monitor, channel prioritization)
Daniele Domenichelli (YARP, ROS-YARP)
Alberto Cardellino (YARP, robot interface, ROS-YARP)
Marco Randazzo (robot interface, firmware)
Andrea Ruzzenenti (simulator, slam)
Marco Accame (firmware)
Valentina Gaggero (firmware)
Alessandro Scalzo (firmware)
Ugo Pattacini
Vadim Tikhanoff
Silvio Traversaro
Francesco Romano
Francesco Nori
Giorgio Metta
Notes: 8 people, mostly technicians, 1 postdoc
Collaborations with other groups

## Slide 72: Thank you